## Slide 1
Simulation of Soil Water Flow
BSEN 5250/6250

## Slide 2
Soil Structure
Sand
Silt
Clay
Stones
Organic Matter
Organisms

## Slide 3
Size of Soil Components

## Slide 4
Soil Types-Natural Resources Conservation Service

## Slide 5
What is the soil type if a soil has 40% sand, 40% silt and 20% clay?
Loam!

## Slide 6
Digital Soil Maps
Widely available on internet
FAO Digital World Soil Database
Course survey maps
Often digital version of hand drawn survey

## Slide 9
Soil Structure and Water Storage

## Slide 11
Gravity Force

## Slide 12
Components of a Soil Water Balance
Infiltration (I)
Drainage (D)
Transpiration (T)
Evaporation (E)
Rainfall
Runoff (R)
Mass Balance Equation

## Slide 13
Runoff and Infiltration – SCS Curve Number Method
Q = 0 for P ≤ Ia
Q = runoff, inches or mm
P = rainfall, inches or mm
S = potential maximum soil moisture retention after runoff begins, inches or mm
Ia = initial abstraction, inches or mm
Ia = 0.2*S
For P > Ia
Note: if P ≤ 0.2*S then Q = 0 and Infiltration = 0

## Slide 14
Calculation of S Term
CN is the SCS Curve Number that impacts infiltration
For English Units, inches
For Metric Units, mm

## Slide 15
Soil Conservation Service Curve Number 2 Table

## Slide 17
HSG Group A (low runoff potential): Soils with high infiltration rates even when thoroughly wetted. These consist chiefly of deep, well-drained sands and gravels. These soils have a high rate of water transmission (final infiltration rate greater than 0.3 in./h).
HSG Group B Soils with moderate infiltration rates when thoroughly wetted. These consist chiefly of soils that are moderately deep to deep, moderately well drained to well drained with moderately fine to moderately coarse textures. These soils have a moderate rate of water transmission (final infiltration rate of 0.15 to 0.30 in./h).
HSG Group C: Soils with slow infiltration rates when thoroughly wetted. These consist chiefly of soils with a layer that impedes downward movement of water or soils with moderately fine to fine textures. These soils have a slow rate of water transmission (final infiltration rate 0.05 to 0.15 in./h).
HSG Group D (high runoff potential): Soils with very slow infiltration rates when thoroughly wetted. These consist chiefly of clay soils with a high swelling potential, soils with a permanent high water table, soils with a claypan or clay layer at or near the surface, and shallow soils over nearly impervious materials. These soils have a very slow rate of water transmission (final infiltration rate less than 0.05 in./h).
Hydrologic Soil Groups
Source: https://en.wikipedia.org/wiki/Runoff_curve_number

## Slide 18
Antecedent Moisture Content
The wetness of the soil influences the amount of runoff
The 5-day antecedent moisture content is used to adjust the CN

## Slide 19
Chart: Antecedent Curve Number
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90
CN1 | 4.4586 | 9.5023 | 15.2542 | 21.875 | 29.5775 | 38.6503 | 49.4949 | 62.6866 | 79.0795
CN3 | 20.354 | 36.5079 | 49.6403 | 60.5263 | 69.697 | 77.5281 | 84.2932 | 90.1961 | 95.3917
Adjusting Curve Number for Antecedent Moisture Conditions
If the soil is dry, runoff decreases, so adjust CN down to compensate (CN1)
If the soil is wet, runoff increases, so adjust CN up to compensate (CN3)

## Slide 20
Source: https://en.wikipedia.org/wiki/Runoff_curve_number
Adjusting Curve Number for Antecedent Moisture Conditions

## Slide 21
Example of Computing Runoff
Given: A Corn field is planted in rows in Alabama. The soil is Hydrologic Group B and the preceding 5-day rainfall is less than 1 inch.
Find: Calculate the runoff and infiltration from a 2 inch rainfall.
Step 1: Determine curve number for antecedent moisture II condition for corn planted in straight rows with good hydrologic conditions for hydrologic group B soil. From Table, CN2 = 78
Step 2: Adjust CN2 for antecedent moisture condition 1 (dry).

## Slide 22
Example of Computing Runoff
Step 1: Determine curve number for antecedent moisture II condition for corn planted in straight rows with good hydrologic conditions for hydrologic group B soil. From Table, CN2 = 78
Step 2: Adjust CN2 for antecedent moisture condition 1 (dry). CN1 = 60
Step 3: Compute Runoff
Infiltration = Rainfall – Runoff = 2 inches – 0.061 inches = 1.94 inches
2 in
0.061 in
1.94 in

## Slide 23
Volume 1 (V1)
V2
V3
V4
V5
V6
Simulation of Water Flow in Agricultural Soils
Layer 0
Layer 1
Layer 2
Layer 3
Layer 4
Layer 5
Layer 6
f0-1 = Infiltration (I)
Layer 7
f1-2
f2-3
f3-4
f4-5
f5-6
f6-7 = Drainage (D)
f1-0 = Evaporation (E)
Transpiration (T1)
T2
T3
T4
T5
T6

## Slide 24
Volume 1 (V1)
Layer 0
Layer 1
f0-1 = Infiltration (I)
f1-2
f1-0 = Evaporation (E)
Volume 2 (V2)
Layer 1
Layer 2
f1-2
F2-3
Transpiration (T1)
T2
Water Mass Balance in Soil Layer

## Slide 25
V1
V2
V3
V4
V5
V6
Layer 0
Layer 1
Layer 2
Layer 3
Layer 4
Layer 5
Layer 6
f0-1 = Infiltration (I)
Layer 7
f1-2
f2-3
f3-4
f4-5
f5-6
f6-7
f1-0 = Evaporation (E)
T1
T2
T3
T4
T5
T6
System of Equations Governing Water Flow

## Slide 26
Euler Solution

## Slide 27
How To Determine Water Flow
Between Soil Layers
Water content is a measure of water in soil
Water content is a “property” of soil
Units are cm3 water per cm3 soil
Water moves through soil
Water content does not move
Water content changes because water moves

## Slide 28
Volumetric Water Content
1 cm
1 cm
1 cm
Water is stored in pore space
Volume of Soil = 1 cm3
Volume of Water = 0.3 cm3
Soil = 1 cm3
Water = 0.3 cm3
0.3 cm
% Water Content = Volumetric Water Content x 100 = 0.3 cm3 / cm3 x 100 = 30%

## Slide 29
Depth of Water Storage
1 foot (12 inches)
3 inches
English Units
Water Depth = 3 in water/foot of soil
Soil Volume = 1 ft * 1 ft * 1 ft = 1 ft3
Water Volume = 0.25 ft * 1 ft * 1 ft = 0.25 ft3
Volumetric Water Content = 0.25 ft3 water / 1 ft3 soil
= 0.25 ft3 / ft3
= 0.25 in3 / in3
Water

## Slide 30
Depth of Water Storage
10 cm
1 m (100 cm)
Water Depth = 10 cm water/m soil
Soil Volume = 1 m * 1 m * 1 m = 1 m3
Water Volume = 0.1 m * 1 m * 1 m = 0.1 m3
Volumetric Water Content = 0.1 m3 water / 1 m3 soil
= 0.1 m3 / m3
= 0.1 cm3 / cm3
Metric Units
Water

## Slide 31
Key Volumetric Soil Water Levels
Lower Limit (LL, cm3 water/cm3 soil) – The volumetric content of water in soil when the roots have extracted all possible water. Note that roots cannot extract all of the water in the soil. This is often referred to as Wilting Point. Estimated as -15 bars of pressure (217 PSI).
Drained Upper Limit (DUL, cm3 water/cm3 soil) – The volumetric water content in soil when the capillary forces holding water within the pore space equals the force of gravity pulling against water molecules. This can be measured by filling the soil profile up and allowing it to drain freely until drainage stops. This is often referred to as Field Capacity. It is estimated at -1/3 bar of pressure (4.7 PSI).
Saturation (SAT, cm3 water/cm3 soil) – This is the maximum volume of water that a particular soil can hold within all its pore spaces.
1 bar = 14.5 PSI

## Slide 32
Soil Water Holding Characteristics
Drained Upper Limit
(field capacity), cm3 / cm3
Saturation, cm3 / cm3
Lower Limit
(wilting point), cm3 / cm3
0.49 cm3 / cm3
0.32 cm3 / cm3
0.22 cm3 / cm3
unavailable water
available water
free flowing water

## Slide 34
Pressure Plate Measurements
Saturation at -0.1 bars
DUL at -0.33 bars
LL at -15 bars

## Slide 35
Drainage of Free Flowing Water
Saturated flow occurs when soil water is above the DUL
Gravity causes water to drain down to the DUL
Three approaches are used to compute water drained per day from saturated layers:
Darcy’s Equation
Saturated Hydraulic Conductivity = cm/hr
Fraction drained per day, %/day
unavailable water
available water
free flowing water
SAT
DUL
LL
48 cm
1 m

## Slide 36
Example of Soil Water Content Over Time
DUL
SAT
Lower Limit
Saturated Drainage
Plant Uptake
Rainfall
Volumetric Soil Water Content, cm3 / cm3

## Slide 37
Chart: Days
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
30%/day | 1 | 0.7 | 0.49 | 0.343 | 0.2401 | 0.16807 | 0.11765 | 0.082354 | 0.057648 | 0.040354 | 0.028248
50% per day | 1 | 0.5 | 0.25 | 0.125 | 0.0625 | 0.03125 | 0.015625 | 0.0078125 | 0.0039062 | 0.0019531 | 0.00097656
70%/day | 1 | 0.3 | 0.09 | 0.027 | 0.0081 | 0.00243 | 0.000729 | 0.0002187 | 6.561e-05 | 1.9683e-05 | 5.9049e-06

## Slide 38
Example of Fraction Daily Drainage Rate
Given: DUL = 0.3 cm3 / cm3 and SAT = 0.5 cm3 / cm3
Volumetric soil water content = 0.45 cm3/cm3
Find: Compute the drainage rate over 3 days if the fraction of drainage under saturated conditions in this soil is 0.5/day (ie. 50% of the excess water drains each day).

## Slide 39
Example: Compute Daily Drainage
Soil water content = 0.45 cm3 / cm3
DUL = 0.3 cm3 / cm3
Free water = 0.45 – 0.3 = 0.15 cm3 / cm3
Drainage rate of free water = 0.5/day
Day 1
Drainage on Day 1 = 0.5/day * 0.15 cm3 / cm3 = 0.075 cm3 / cm3 drained.
Fraction drained today
Free water above DUL
Water content at end of Day 1 = 0.45 – 0.075 = 0.375 cm3 / cm3
Water at beginning of day 1
Drainage today
Water content after Day 1
Water available to drain at end of Day 1 = 0.375 – 0.3 = 0.075 cm3 / cm3
DUL

## Slide 40
Drainage on Day 2 = 0.5/day * 0.075 cm3 / cm3 = 0.0375 cm3 / cm3 drained.
Fraction drained today
Free water above DUL
Water content at end of Day 1 = 0.375 – 0.0375 = 0.3375 cm3 / cm3
Water at beginning of day 2
Drainage today
Water content after Day 2
Water available to drain at end of Day 2 = 0.3375 – 0.3 = 0.0375 cm3 / cm3
DUL
Drainage on Day 2

## Slide 41
Drainage on Day 3 = 0.5/day * 0.0375 cm3 / cm3 = 0.01875 cm3 / cm3 drained.
Fraction drained today
Free water above DUL
Water content at end of Day 1 = 0.3375 – 0.01875 = 0.319 cm3 / cm3
Water at beginning of day 3
Drainage today
Water content after Day 3
Water available to drain at end of Day 2 = 0.319 – 0.3 = 0.019 cm3 / cm3
DUL
Drainage on Day 3
With a drainage rate of 0.5/day, most of the free water has drained in 3 days

## Slide 42
Example of Soil Water Content Over Time
DUL
SAT
Lower Limit
Saturated Drainage
Plant Uptake
Rainfall
Volumetric Soil Water Content, cm3 / cm3

## Slide 43
Chart: Fraction Daily Drainage
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
30%/day | 1 | 0.7 | 0.49 | 0.343 | 0.2401 | 0.16807 | 0.11765 | 0.082354 | 0.057648 | 0.040354 | 0.028248
50% per day | 1 | 0.5 | 0.25 | 0.125 | 0.0625 | 0.03125 | 0.015625 | 0.0078125 | 0.0039062 | 0.0019531 | 0.00097656
70%/day | 1 | 0.3 | 0.09 | 0.027 | 0.0081 | 0.00243 | 0.000729 | 0.0002187 | 6.561e-05 | 1.9683e-05 | 5.9049e-06
Selection of fraction daily drainage rate for free water above the DUL can be guided by field data for specific soil types.

## Slide 44
Where To Find Soil Properties
USDA Soil Survey
http://websoilsurvey.sc.egov.usda.gov/App/HomePage.htm

## Slide 45
Chart: General Soil Characteristics
| Sand | Loamy Sand | Sandy Loam | Loam | Silt Loam | Sandy Clay Loam | Sandy Clay Loam | Clay Loam | Silty Clay Loam | Silty Clay | Clay Loam
DUL
LL
AWC
LL, cm3/cm3 | 0.041667 | 0.066667 | 0.091667 | 0.11667 | 0.15 | 0.18333 | 0.15 | 0.18333 | 0.2 | 0.2 | 0.21667
DUL, cm3/cm3 | 0.1 | 0.15833 | 0.20833 | 0.26667 | 0.3 | 0.29167 | 0.28333 | 0.31667 | 0.35833 | 0.4 | 0.4
AWC, cm3/cm3 | 0.058333 | 0.091667 | 0.11667 | 0.15 | 0.15 | 0.10833 | 0.13333 | 0.13333 | 0.15833 | 0.2 | 0.18333

## Slide 46
Water holding capacity is 1-10” water in the top 5’ of soil

## Slide 47
Soil Properties in Iowa
Note the high water holding capacity of these soils (13” per 5’ of soil)

## Slide 48
V1
V2
V3
V4
V5
V6
Layer 0
Layer 1
Layer 2
Layer 3
Layer 4
Layer 5
Layer 6
f0-1 = Infiltration (I)
Layer 7
f1-2
f2-3
f3-4
f4-5
f5-6
f6-7
f1-0 = Evaporation (E)
T1
T2
T3
T4
T5
T6
We can now compute drainage if water content is above the DUL.
When water content is between the DUL and LL, the, only way water leaves the layer is through root water uptake
Soil Water Dynamics in Soil Layer

## Slide 49
Free Drainage – Hydraulic Conductivity Approach
unavailable water
available water
free flowing water
SAT= 0.48 cm3 / cm3 = 48 cm water in 1 m soil
DUL = 0.3 cm3 / cm3 = 30 cm water in 1 m soil
LL=0.10 cm3 / cm3 = 10 cm water in 1 m soil
48 cm
1 m
Saturated Hydraulic Conductivity – cm/day or in/day
Distance of water flow each day
Darcy’s Law

## Slide 50
Darcy’s Law
J = water flux, cm/day or cm/hr
Q = volume of water flow, cm3
A = cross sectional area of soil column, cm2
t = time, day or hr

## Slide 51
Permeability Class | Rate (in/hr) | Rate (cm/hr)
Very Rapid | > 10 | > 25.4
Rapid | 5 to 10 | 12.7 to 25.4
Moderately rapid | 2.5 to 5 | 6.35 to 12.7
Moderate | 0.8 to 2.5 | 2.03 to 6.35
Moderately Slow | 0.2 to 0.8 | 0.5 to 2.03
Slow | 0.05-0.2 | 0.12 to 0.5
Very Slow | < 0.05 | < 0.12
Permeability Classification System

## Slide 52
Impermeable Soil Layers
Tile drainage properties
Hardpan
characteristics
Impeding layer
Layer properties: DUL, LL, SAT, Ksat

## Slide 53
Evapotranspiration: Blaney-Criddle Method
ET = k P (0.46 * T + 8.43)
ET = evapotranspiration, mm/month
k = monthly crop evapotranspiration coefficient
T = mean monthly temperature, oC
P = monthly percent of total daytime hours
of the year (decimal percent)

## Slide 54
Mean Monthly Temperature
All temperatures in units of oC

## Slide 55
Mean Daily Percentage of Annual Daytime Hours for Different Latitudes
Source: FAO, Irrigation Water Management. www.fao.org
These numbers are daily values. Need to multiply by number of days in the month to convert to P coefficient in Blaney-Criddle Formula

## Slide 56
Monthly Crop Evapotranspiration Coefficient, k
Changes during year to represent different crop needs based on crop leaf area and environment

## Slide 57
Source: http://www.fao.org/docrep/x0490e/x0490e0b.htm#tabulated kc values
FAO Crop Coefficient Table
See handout

## Slide 58
Blaney-Criddle ET Example
Given: Corn growing in Mobile Alabama (Latitude 30o N). The average temperature during July is 29 o C. The crop has a full canopy and is in the middle of its growth cycle.
Find: Compute the monthly and daily evapotranspiration
Solution:
From FAO Table, at 30oN latitude in July, mean daily percent of annual daytime hours is 0.31
0.31 percent/day * 31 days in July = 9.61 % of annual daytime hrs

## Slide 59
ET = k P (0.46 T + 8.43)
= 1.15 * 9.61 (0.46*29 + 8.43)
= 240.6 mm per month
240.6 mm/month * 1 month/31 days = 7.76 mm/day
From FAO Table, k = 1.15 for maize during mid growth
Blaney-Criddle ET Example

## Slide 60
Root Water Uptake
Impeding layer
Layer properties: DUL, LL, SAT, Ksat, RHF

## Slide 61
Root Length Volume is cm root per cm3 soil
Root Length Volume
RLV = 5 cm root/cm3 soil
RLV = 4 cm root/cm3 soil
RLV = 3 cm root/cm3 soil
RLV = 2 cm root/cm3 soil
RLV = 1 cm root/cm3 soil
RLV = 0
1.5 m

## Slide 62
Root Length Volume
RLV = 5 cm root/cm3 soil
RLV = 4 cm root/cm3 soil
RLV = 3 cm root/cm3 soil
RLV = 2 cm root/cm3 soil
RLV = 1 cm root/cm3 soil
RLV = 0
1.5 m
2.7 Miles of Roots!

## Slide 63
Source: An Introduction to Crop Physiology by Milthorpe and Moorby. 1979.
Twelve Miles of Roots Per m2 Soil!

## Slide 64
RLV = 5 cm root/cm3 soil
RLV = 4 cm root/cm3 soil
RLV = 3 cm root/cm3 soil
RLV = 2 cm root/cm3 soil
RLV = 1 cm root/cm3 soil
RLV = 0
Total RLV = 5+4+3+2+1 = 15
Proportion of ET Demand
5/15 = 0.33
4/15 = 0.27
3/15 = 0.20
1.5 m
2/15 = 0.13
1/15 = 0.067
Proportion of Water Uptake From Each Soil Layer
Simple approach is to use weighted average of RLV to compute water uptake from soil layer

## Slide 65
Soil Surface
Water Table in June/July
Water Table in Aug/Sept
Rainfall
Run-on
Runoff
Infiltration
Drainage
Leaching
Roots
Dynamics of Water Availability

## Slide 66
Drought Tolerant Crop Varieties
Increased carbon partitioning to roots
Deeper root systems
Regulated stomata under stress